## Slide 1: Advanced Pipelining
Pavel Kryukov
01/12/2017

## Slide 2: Traps

## Slide 3: Exceptions and Interrupts
Term “exception” is used for internal sudden events:
  Division by zero
  Register overflow
  Unknown opcode
External events are “interrupts”.
  I/O request
  HW failure
In MIPS terminology “interrupts” and “exceptions” are “traps”
Otherwise in x86

## Slide 4: Exception handling
On exception, MIPS ISA defines following actions:
  Save IP of instruction that caused exception to EPC register
  Save exception type to Cause register
  Call OS subroutine (handler) by predefined address
MIPS allows “vector exception” — different handlers may be used for different exceptions

## Slide 5: MIPS Exception types
ID stage:
  Unknown instruction
EX stage:
  Unsupported syscall
  Arithmetic overflow
  Division by zero
  Explicit trap (teq, tne and similar instructions)
MEM stage:
  Unaligned load/store address
  Unaligned return address
  Incorrect load/store address
  Incorrect return address
etc.

## Slide 6: Adding exceptions to Single-Cycle MIPS
Exception Control
InvalidOpcode
Overflow/Div0
InvalidAddress
EPC
Cause
CauseCode
IsException
Vector
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
CondCode
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
Add
Add
PC
4
0
1
m
u
x
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Control
CondCode

## Slide 7: Pipeline issue 1: simultaneous exceptions
Several instructions can generate exceptions on different stages but on the same cycles
Solution: prioritize exceptions on the later stages
F
D
E
M
F
D
E
F
D
F
lw $r3, $zero(0x0)
div $r2, $zero
<invalid opcode>

## Slide 8: Pipeline issue 2: flushing pipeline
Pipeline has to cancel all consequent instructions to have correct architecture state
Not a problem since we handle branch mispredictions already
F
D
E
M
W
F
D
E
M
F
D
E
F
D
F
F
D
E
M
W
Some expections require writeback
W

## Slide 9: Pipeline issue 3: speculative instructions
We may execute exception-causing instruction after mispredicted branch
beq
<invalid opcode>
lw $r1, $r2(0x0)
lw $r3, $r1(0x0)
F
D
E
F
D
F
beq
<inv>
lw
F
D
E
M
F
D
E
lw
lw
Not an exception!
M
E
D
F
lw

## Slide 10: Cumulative solution
The cumulative solution is to move exception information through the pipeline
Perform exception handling only on the WB stage
decoder
EPC
Memory
0
1
Registers
ALU
Sign ext
0
1
Memory
1
0
Memory
PC
Add
4

## Slide 11: Complex pipeline

## Slide 12: Unified Pipeline
So far only a unified pipeline have been considered where each instruction takes the same number of cycles to execute
The real latency of instructions can differ significantly:
  Memory systems with variable access time
  Long latency calculations (multiplication, division, floating point operations, etc.)
Increasing of the clock cycle to fit the longest instruction and thereby keeping pipeline unified may be inefficient
wait
F
wait
W
D
wait
E longest
M
wait
E medium
E short
Most of instructions are shorter and do not need such long clock cycle
Sync signal
(clocks)
time
4ns
8ns
12ns
16ns
20ns

## Slide 13: Unified Pipeline
The problem is resolved by splitting execution into more stages
F | D | E1 | E2 | E3 | E4 | M | W | 
F | D | E1 | E2 | E3 | E4 | M | W |  | 
 | F | D | E1 | … |  |  |  |  | 
 |  | F | D | E1 | … |  |  |  | 
 |  |  | F | D | E1 | … |  |  | 
 |  |  |  | F | D | E1 | … |  | 
 |  |  |  |  | F | D | E1 | … | 
 |  |  |  |  |  | F | D | E1 | …
 |  |  |  |  |  |  | F | D | E1
F |  |  |  | D |  |  |  | E longest | M |  |  |  | W |  |  | 
F | D | E1 | E2 | E3 | E4 | M | W | 
But, for better overlapping of short instructions a complicated forwarding is required (too many stages to take a value from)
Unfeasible makes the concept of a unified pipeline inefficient
  Full forwarding are too huge and slow → increase the clock cycle
  Without full forwarding there will be bubbles in the pipeline → high CPI
Only this instruction can safely read its sources from the Register File

## Slide 14: Non-Unified Pipeline
Ok, let’s make non-unified pipeline
R1 ← R2 / R3
...
R1 ← R2 + R3
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |  | 
F | D | E1 | E2 | E3 | E4 | W |  |  |  |  | 
 | F | D | … |  |  |  |  |  |  |  | 
 |  | F | D | E1 | W |  |  |  |  |  | 
– Yes, out-of-order instruction completion, which may lead to writing wrong register value
The add writes R1 before the division, i.e. the next instruction will consume the wrong value of R1
F | D | E1 | M | W | 
F | D | E1 | E2 | E3 | E4 | W | 
F | D | E1 | E2 | W | 
Any problems?
F | D | E1 | W | 
Simple arithmetic
Memory accesses
Complex arithmetic
Floating point arith.

## Slide 15: Complex Pipeline
Decision is using non-unified (i.e., complex) pipeline, but fix somehow the problem with out-of-order completion
Need track not only true dependences, but also Write-After-Write (WAW) ones:
Code Example:
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
3. R1 ← R2 + R3
True dependence (Read-After-Write)
False dependence (Write-After-Write)
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
1. R1 ← MEM[Addr]
3. R1 ← R2 + R3
Anti-dependence (Write-After-Read)
2. R4 ← R1 * R3
3. R1 ← R2 + R3
Not a problem for now, as instruction cannot write the results until all the previous read their sources either from the RF or bypasses
Not a problem for now, as all instruction are issued in-order:
the result is in the RF or available through bypass
Need to obey this kind of dependencies

## Slide 16: Scoreboard for tracking WAW
The solution is “book-keeping” on the issue stage (so-called scoreboarding)
  Know everything: whether a register is being calculated or available in the RF/Bypass, when it will be ready, which unit processes it, etc.
 | 5 | 4 | 3 | 2 | 1 | In Bypass | In RF
R0 |  |  |  |  |  |  | 
R1 |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
R31 |  |  |  |  |  |  | 
1
1
1
1
Number of cycles till writeback
on writeback?
in RF?
On issue stage check the table:
  Check WaW
    There is no operation that will write the same register later than the current instruction
  Check resource conflict on WriteBack
    There is no operation that will write any register in the same cycle
  If all conditions are satisfied:
    Update the table by information on the destination
    Go to the next stage
  If not – stall the instruction
Shift all “1” right every cycle
Example of a scoreboard table:
Algorithm:

## Slide 17: Superscalar pipelines

## Slide 18: Superscalar processors
Single-cycle and pipelined processors are unified to scalar class as they process 1 instruction in 1 cycle
Superscalar CPU processes 2 or more instructions in each cycle with additional pipeline, extracting ILP (instruction level-parallelism)
F
D
E
M
W
PC
time
4ns
8ns
12ns
16ns
PC + 4
F
D
E
M
W
PC + 8
F
D
E
M
W
F
D
E
M
W
PC + 12
PC + 16
F
D
E
M
W
F
D
E
M
W
PC + 20

## Slide 19: Approach 1: dynamic scheduling of Pentium®
2 pipelines: U and V
      V pipeline is reduced — it can’t execute every instruction
      V pipeline is used only for instruction independent from previous
Decoder decides whether to use V pipeline or not
U-E
U-M
U-W
F
PC
PC + 4
time
4ns
8ns
12ns
16ns
V-E
V-M
V-W
U-M
U-W
D
PC + 8
F
PC + 12
U-E
U-M
U-W
D
PC + 16
F
PC + 20
U-E
D
F
U-E
U-M
U-W
D
V-E
V-M
V-W

## Slide 20: Approach 2: VLIW (Itanium® and E2K)
Compiler merges independent instructions to “bundles”
Each bundle is a single instruction for CPU (Very Long Instruction Word)
PC
E1
F
D
W
AGU
M
FP
E2
E1’
FP
E2’
E1
F
D
W
AGU
M
FP
E2
E1’
FP
E2’
PC + 16

## Slide 21: Approach 3: vectorization
Bind independent data to vectors
Each component of vector is processed independently
PC
F
D
W
FP-G
FP-G
FP-B
FP-A
FP-R
FP-B
FP-A
FP-R
F
D
W
FP-G
FP-G
FP-B
FP-A
FP-R
FP-B
FP-A
FP-R
PC + 4

## Slide 22: Summary
VLIW has several disadvantages:
  Compiler often adds “nops”
  Delay in one instruction delays whole bundle
Dynamic scheduling is not efficient:
  Many instructions are dependent on previous ones
Vectorization is limited:
  Many instructions are scalar
Modern superscalar CPUs use much more powerful method to extract ILP
  out of this lecture scope

## Slide 23: Thank You Q/A