## Slide 1: Performance and Power
Pavel Kryukov
08/12/2017

## Slide 2: Refresher: Basic Design Tradeoffs
All three are very important
It is extremely hard to create a feature that improves all factors
Different products (mobile, desktop, etc.) require different balance
Performance
(speed)
Cost
(complexity, area)
Power
(energy consumption and dissipation)

## Slide 3: Performance

## Slide 4: Performance
What does performance depend on?
Golden rule of CS

## Slide 5: Increasing Performance
How can we increase it?
Better SW: algorithms, optimizations, ISA, etc.
Better CD: faster circuits, smaller transistors, etc.
Better uArch: pipelining, caching, prediction, etc.
But, need better CD to enable these approaches
(e.g., more transistors)

## Slide 6: Refresher: Pipeline speedup
Pipelining does not reduce the latency of a single workload, it increases the total throughput (number of completed workload per time unit)
Pipeline throughput(=rate) is limited by the slowest stage
Potential speedup is:
In ideal case, all stages have the same length:

## Slide 7: Ways to increase speedup
  Partition the pipe to many pipe stages
  Balance the work in the pipe stages: make the longest pipe stage to be as short as possible
Latches increase overall latency

## Slide 8: Pipeline Timing Model
Assuming that instructions are executed in L seconds
Each latch adds s delay
If pipeline has N stages, overall execution time is
Each stage is seconds long
F
D
E
M
W
L
= L + 2s
= L + 3s
s
L/3
s
L/3
s
L/3
s
L/2
s
L/2
s

## Slide 9: Performance with Latches
Every cycle is long
In ideal case, IPC = 1 for pipeline
Performance is
Infinite performance is impossible
The best result is achieved if cycle contains nothing but latches

## Slide 10: Hardware cost
Furthermore, latches require additional HW
Overall cost is
G
Q
G/2
Q
G/2
G/3
Q
G/3
G/3
Q
Q
Q

## Slide 11: Cost/Performance Trade-off
In 1981, Peter M. Kogge used following metric to find optimal pipeline:
Derivation by N can be used to find minimum:
HW cost is not very important today
Most of CPUs are superscalar

## Slide 12: Improving model: adding BTB Impact
Branch mispredicts stall some fraction (γ) of pipeline
Since they are rare, in average CPI delta is lower:
In general, “alpha” parameter is a function of selected uArch:
    how good branches are predicted;
    how mispredicts affect pipeline;
    bypassing levels;
    cache hit rate, out-of-order effects etc.

## Slide 13: Amdahl’s Law
If a fraction F of the program is accelerated by a factor S, and the remainder of the program is unaffected, then:
T’=T x [ (1-F) + ]
Speedup =
Corollaries:
  There is a limit of how much speedup is achieved
    Speedupmax =
  Diminishing returns
  Make common case fast
T
T’

## Slide 14: Examples of Amhdal’s Law
Assuming branch prediction accuracy is 50%
20% of instructions are branches
Increasing BPU accuracy to 90%
Improving BPU accuracy by 40% → CPI increase is only 18%

## Slide 15: Improving model: adding superscalar
In superscalar CPUs ideal CPI depends on width
Overall, we have an equation for performance
Let’s use clock time for simplicity

## Slide 16: Maximum performance
Performing derivation by t:
Finding maximum performance:

## Slide 17: Intel CPUs timeline
Chart: nm/MHz
| 1978 | 1982 | 1985 | 1989 | 1993 | 1995 | 1997 | 1999 | 2000 | 2002 | 2004 | 2006 | 2008 | 2011 | 2013
Freq | 0 | 8 | 16 | 25 | 60 | 150 | 233 | 450 | 1400 | 2000 | 3400 | 3000 | 3000 | 3000 | 3000
Process | 3000 | 1500 | 1000 | 1000 | 800 | 600 | 350 | 250 | 180 | 130 | 90 | 65 | 45 | 22 | 22
Pipeline Depth | 2 | 3 | 3 | 5 | 5 | 12 | 12 | 12 | 20 | 20 | 31 | 12 | 20 | 14 | 14
8086
80286
80386
80486
Pentium
Pentium Pro
PII
PIII
P4
Prescott P4
What happened?

## Slide 18: Power

## Slide 19: Power
Why is power important?
    Less power -> smaller battery -> smaller/cheaper devices
    Less power -> less money for electricity
Power Wall is reached
    The maximum power dissipation that cooling systems can handle is reached
    We cannot spend more power even if we want
Nuclear reactor? No, power supply for a large data center

## Slide 20: Power Consumption in CMOS
Gate
Source
Drain
Source
Drain
0
1
Gate
Gate
Output
n
n
n
p
p
p
Input
1
+
+
-
-
0
Vcc
1
Input
Output
No current in static state, i.e. there is no power consumption
Current exists only at switch from one state to another to recharge the capacities
No connection between the power supply and the ground

## Slide 21: Recharging Power

## Slide 22: Dynamic power
Dynamic power in consumed since transistors change state:
Keep in mind that clock signals are included in dynamic power
Some power is lost due to “crowbars”
~80% of consumed power
average amount of transistors
dynamic capacity
Voltage
frequency
1
0

## Slide 23: Static power
Static power is consumed by leakage
Area S depends on:
  number of pipeline stages N (more latches required)
  issue width W
  branch prediction, caches etc. — α
Leakage current j depends on technical process
~20% of consumed power
leakage current
area

## Slide 24: Performance/Power balance
Depending on market target, we may optimize:
    performance (IPS)
    power (Watts)
    energy = power / IPS (Joules)
    dissipation = power / area (Watts / cm2)
New features are added to CPU regarding to select target
Example 1: deeper pipelining increases power consumption:
    higher frequency increases dynamic power
    new latches increase both static and dynamic power
Example 2: issue width increases power in ~W times

## Slide 25: Overcoming Power Wall
Power saving features
  slow down performance, but save energy/power
Multicore systems
  shrink the core, but put them on single chip
Simultaneous multithreading
  do more tasks on the same area

## Slide 26: Thank You Q/A