## Slide 1: Caches, pt. I
Pavel Kryukov
10 February 2017

## Slide 2: Memory Is Slow
CPU
DRAM
60% per year
(Doubles every 1.5 year)
9% per year
(Doubles every 10 year)
Performance gap

## Slide 3: Why is memory slow?
A1: Memory uses DRAM technology, while registers are SRAM
  DRAM is slower, but cheaper
  This is not the answer: may we use SRAM for memory?
A2: Memory transistors are smaller, therefore they are slower
  Again: may we use big transistors for memory?
DRAM cell
SRAM cell

## Slide 4: Correct answer is: area
Large memory arrays have large area, so wires have to be long
Large memory cannot be fast. Fast memory cannot be large.

## Slide 5: Refresher: Pipeline limitations
 |  |  | F | D | E | M | W |  | 
 |  |  |  | F | D | E | M | W | 
 |  |  |  |  | F | D | E | M | W
Max speed of the pipeline is one instruction per clock
It is rare achievable in in-order processors due to dependencies among instructions and long latency operations
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
M | W
Load from the memory

## Slide 6: Memory Hierarchy
Main memory is large, but too slow
Small memory is fast, but cannot hold all required data
Solution: take the best of both and combine
Memory hierarchy provides visibility that memory is usually fast
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 7: Real life example: Logistics
Your shop
Factory
Shop store
Storehouse
Large storehouse
The delay is decreased, but the cost is increased

## Slide 8: Real life example: bookshelf
A-B | C-D | E-F | G-H | I-J | … | … | … | … | … | Y-Z
The first letter in the name of the author
Places for books
Your table
fast
slow
Your bookshelf
City library

## Slide 9: Why Does It Work?
Temporal Locality (Locality in Time):
  If an item is accessed, it will tend to be accessed again soon
  Example: code and variables in loops
→ Keep recently accessed data closer to the processor
Spatial Locality (Locality in Space):
  If an item is accessed, nearby items tend to be accessed soon
  Example: scanning an array
→ Move contiguous blocks closer to the processor
Locality + smaller HW is faster memory → hierarchy

## Slide 10: Cache: Main Idea
The cache holds a small part of the entire memory
  Need to map parts of the memory into the cache
Main memory is virtually partitioned into lines
  Typical block size is 32 to 64 bytes
  Blocks are aligned
Memory
Cache
#line
#line
The cache holds data by lines
  Only a subset of the blocks is mapped to the cache at a given time
Address of lines is used as a key
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
91 | 
4 | 
5 | 

## Slide 11: Cache Lookup
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
2 | 
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
4?
4
hit
CPU

## Slide 12: Cache Lookup
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
93?
4
miss
2
93
93?
CPU
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
  The requested line is not in the cache
  Need to fetch it from the main memory (slow) and fill the cache
  May need to evict another line from the cache to free space for the new one

## Slide 13: Fully Associative Cache
data
Line may be mapped to any cache entry
  Lookup line in all entries
Address is partitioned to
  Offset within a line (byte#)
  Line # (so-called tag)
Each cache entry has a tag
  All tags are compared to the line# in parallel
  If one of the tags matches the line#, we have a hit
63
0
…
hit/miss
=
=
=
…
…
Tag
Array
Data
Array
64 | 5 | 0
Tag = line# | Offset | 
Address
0 | 
1 | 
… | 
511 | 

## Slide 14: Direct Mapped Cache
Line is mapped to the fixed entry only
  Lookup line in one entry
Address is partitioned to
  Offset within a line (byte #)
  Set (fixed cache entry #)
  Tag (works as a key)
Conflicts are possible
  If several lines are mapped to the same entry, only one can reside in the cache
data
0 |  |  | 
1 |  |  | 
… |  |  | 
511 |  |  | 
63
0
Tag Array
Data
Array
Address
64 | 14 |  | 5 | 0
Tag | Set |  | Offset | 
…
hit/miss
=
set#

## Slide 15: Memory Layout: Direct Mapped Cache
tag#
Memory is virtually partitioned
  into lines
    line size = 2 ^ offset_size
  lines grouped into slices
    # of lines in slices = 2 ^ set_size
    slice size = # of lines in slice * line_size = cache size
  slice # = tag value
  line # inside a slice = set value
…
cache size
cache size
cache size
cache size
Memory Space
set#
set#
set#
set#
Mapped to the same set
 | Offset
 | Set | Offset
Tag | Set | Offset
0
64
Disadvantage is line evictions due to set conflicts

## Slide 16: 2-Way Set Associative Cache
Conflicts are harmful → multi-ways cache is a solution
Each set holds two entries (way 0 and way 1)
  Each line can be mapped into one of two entries in the appropriate set
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #1
set#
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #0
set#

## Slide 17: 2-Way Set Associative Cache
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 | 
1 | 
… | 
255 | 
63
0
way #0
way #0
set#
hit/miss
=
0 | 
1 | 
… | 
255 | 
set#
way #1
=
63
0
way #1
Tag Array
Data Array
MUX
data

## Slide 18: Memory Layout: Multi-Way Cache
Memory is virtually partitioned almost the same as in direct map cache
  The only difference is slice size
    slice size = cache size / # of ways
Compared to direct map cache
  Decrease slice size → increase # of slices → increase # of lines mapped to the same set
  But in each set we can have multiple lines (= # of ways) at a given time
Example: 32KB, 8 ways, 64B line
…
way size
Memory Space
set#
Mapped to the same set
64 | 11 |  | 5 | 0
Tag | Set |  | Offset | 
way size = 32KB / 8 = 4KB
# of sets = 4KB / 64B = 64
address

## Slide 19: Memory Layout: Multi-Way Cache
Slice is Nx smaller
For fully-associative cache N is equal to cache size in lines
For direct mapped cache N == 1
Address partitioning formulas:
63 | Y |  | X | 0
Tag | Set |  | Offset | 
X = log(block_size)
Y = log(cache_size / N)
…
slice
set #
Mapped to N cache lines

## Slide 20: Cache Performance
Terms:
  Miss Rate = Misses / total CPU request
  Hit Rate = Hits / total CPU request = 1 – Miss Rate
Cache goal is decreasing average memory access time (AMAT)
  AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
  AMAT ≈ Hit Time + Miss Rate * Miss Penalty
Example:
  HitRate ≈ 0.9, HitTime ≈ 4 clk, MissRate ≈ 0.1, MissPenalty ≈ 200 clk, then…
  AMAT = 0.9 * 4 + 0.1 * 200 = 23.6 clk
  AMAT w/o cache = 200 clk
  About 10x improve!

## Slide 21: Multi-Level Caches
L1 cache: AMAT ≈ HitTimeL1 + MissRateL1 * MissPenaltyL1
L2 reduces L1 miss penalty – saves access to memory
Now, on L1 miss we access L2, but not memory
  MissPenaltyL1 ≈ HitTimeL2 + MissRateL2 * MissPenaltyL2
L2 Cache is larger (better HitRate), but has higher latency
Example:

## Slide 22: Three Types of Cache Misses (3-C)
Compulsory misses
  Those that occurs even in a infinite cache
  First access to data
  So-called cold misses
Capacity misses
  Those that occurs in an fully associative cache
  Workset is larger than the cache size
Conflict misses
  Difference between fully associate and direct mapped cache
  The size of the cache is enough, but the problem is in line mapping to sets
Compulsory
Conflict
Capacity
Miss Rate = F(Cache Capacity, Associativity)

## Slide 23: Code optimizations

## Slide 24: Merging Arrays
Merge arrays into an array of compound elements
  Before: two sequential arrays
int val[SIZE];
int key[SIZE];
  After: One array of structures
struct merge {
int val;
int key;
} merged_array[SIZE];
Reduce conflicts between val and key
Improves spatial locality

## Slide 25: Loop Fusion
Combine loops that have same looping and work with the same memory
  Assume each element is 8 bytes, 32KB cache, 64 B/line
  for (i = 0; i < 10240; i++)
  a[i] = 1 / a[i];
  …
  for (i = 0; i < 10240; i++)
  sum = sum + a[i];
  Fuse the loops
  for (i = 0; i < 10240; i++) {
  a[i] = 1 / a[i];
  sum = sum + a[i];
  }
Improves temporal locality

## Slide 26: Loop Interchange
Change loops nesting to access data in order stored in memory
  Two dimensional array in memory:
x[0][0] x[0][1] … x[0][99] x[1][0] x[1][1] …
  Before:
  for (j = 0; j < 100; j++)
  for (i = 0; i < 5000; i++)
  x[i][j] = 2 * x[i][j];
  Improves spatial locality
  Sequential accesses instead of striding through memory every 100 words
  for (j = 0; j < 100; j++)
  After:
  for (i = 0; i < 5000; i++)
x[i][j] = 2 * x[i][j];
  for (i = 0; i < 5000; i++)
  for (j = 0; j < 100; j++)
  x[i][j] = 2 * x[i][j];

## Slide 27: “Stop using linked lists”
Linked lists have no spatial locality
  → cache handles them worse than arrays
  → O(N) operation with array is much faster than O(N) operation with list
Example: random insert after linear search
https://kjellkod.wordpress.com/2012/02/25/why-you-should-never-ever-ever-use-linked-list-in-your-code-again

## Slide 28: End of Pt. I