## Slide 1: Caches, part II
Igor Smirnov
17 February 2018

## Slide 2: Improving Cache Performance

## Slide 3: Refresher: Memory Hierarchy
Main memory is large, but too slow
Luckily, there are temporal and spatial locality in our workloads
Memory hierarchy provides visibility that memory is usually fast
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 4: Refresher: Caches
Three types of caches
  Fully Associative: no conflict, but slow and complex HW
  Direct MAP: fast and simple HW, but many conflicts
  Multi-Way: something in between (more ways → closer to fully associative)
Example: 32KB, 8 ways, 64B line
To estimate performance use average access time
    AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
64 | 11 |  | 5 | 0
Tag | Set |  | Offset | 
way size = 32KB / 8 = 4KB
# of sets = 4KB / 64B = 64
address
→

## Slide 5: Refresher: Three Types of Cache Misses (3-C)
Compulsory misses
  Those that occurs even in a infinite cache
  First access to data
  So-called cold misses
Capacity misses
  Those that occurs in an fully associative cache
  Workset is larger than the cache size
Conflict misses
  Difference between fully associate and direct mapped cache
  The size of the cache is enough, but the problem is in line mapping to sets
Compulsory
Conflict
Capacity
Miss Rate = F(Cache Capacity, Associativity)

## Slide 6: Multi-Level Caches
L1 cache: AMAT ≈ HitTimeL1 + MissRateL1 * MissPenaltyL1
L2 reduces L1 miss penalty – saves access to memory
Now, on L1 miss we access L2, but not memory
  MissPenaltyL1 ≈ HitTimeL2 + MissRateL2 * MissPenaltyL2
L2 Cache is larger (better HitRate), but has higher latency
Example:

## Slide 7: Prefetching
Prefetching – predict future memory accesses
Instruction Prefetching
  On a cache miss, prefetch sequential cache line
Data Prefetching
  Next sequential: on a cache miss, prefetch sequential cache line
  Stride: remember the repetitive step of a load and prefetch data in advance
  General direction: even if there is no fixed stride can understand general direction and prefetch along it
Software Prefetching: special prefetching instructions
Prefetch Limitations
  Prefetching relies on extra memory bandwidth
  Too aggressive / inaccurate prefetching slows down demand fetches

## Slide 8: Metrics
Accuracy
  Portion of prefetched lines which eventually become demand-hits
Coverage
  Reduction of number of demand misses
Timeliness
  Reduction of demand miss time
For L1 cache prefetch schemes with high accuracy are used
Bigger caches usually leverage schemes with higher coverage

## Slide 9: Next sequantial
On a cache miss, prefetch sequential cache line (± 64 bytes)
Prefetch metrics:
  Moderate accuracy
  Low coverage
  Lack of timeliness (prefetch performed too late)
Simple HW
Works well for instructions prefetch
“Fallback" if more complex methods not available
  lw $t0, 0x0($t1)
prefetch 0x40($t1)

## Slide 10: Stride detection
HW detects the repetitive step of a load and prefetch data in advance
Prefetch metrics:
  High accuracy (for long loops)
  Low coverage
  Highly timeliness
Issues with unrolled loops
  Initially single load operation occupies multiple entries in detector
  0x00402f0: lw $t0, 0x20($t1)
  0x00402f4: add $t2, $t2, $t0
  0x00402f8: addi $t1, $t1, 0x100
  0x00402fc: beq $t1, $t3, -4
IP | Stride | Last address
0x00402f0 | 0x100 | 0x00f4180
prefetch 0x00f4280
prefetch 0x00f4380
Detector

## Slide 11: Stream detection (1)
HW detects stream with the repetitive step
  Similar to the previous technique, but without reference to IP
Example:
0xba20200
0x3cf1140 0xba203с0
0x3cf1100
0x3cf10c0
0x3cf1080
0xba20740
0xba20900
...
prefetch 0xba20ac0
prefetch 0x3cf10c0
Base address | Stride | Last address
0xba20200 | +0x1c0 | 0xba20900
0x3cf1140 | −0x40 | 0x3cf1080

## Slide 12: Stream detection (2)
Stream detection without repetitive step
  In case load pattern not found, but the direction was predicted – load everything following this direction
Prefetch metrics:
  Low accuracy
  High coverage
  Highly timeliness
0xba20200 0xba20340
0xba203a0
0xba204с0
0xba20520
...
prefetch 0xba20ac0
prefetch 0x3cf10c0
Base address | Stride | Last address
0xba20200 | ???? | 

## Slide 13: Writing and Replacement Policies

## Slide 14: Cache Line Replacement
When miss occurs need to free space in a cache for a new line
Direct mapped cache
  A new line is mapped to a single entry → evict old line from the entry
N-way set associative cache
  Choose a victim from all ways in the appropriate set, but how?
FIFO (First In First Out) replacement
  Easy to implement in HW, but can violate temporal locality
LRU (Least Recently Used) replacement
  Evict the most unused line (was not accessed longer than other)
  Good temporal locality, but complex HW → use simplified pseudo-LRU

## Slide 15: Pseudo-LRU
Pseudo-LRU is a good approximation of LRU with a binary tree
Each node stores information about which of the descendants was recently used
L
R
L
A
B
C
D
R
L
L
A
B
C
D
Request «B»
L
R
R
A
B
E
D
R
R
L
A
B
C
D
Request «A»
Request «E»

## Slide 16: Counterexample
Sometimes there is no temporal locality
  Example: read of large data array (data size >> cache size)
In case of LRU the second loop will always ‘miss’
If data eviction follows MRU policy (most-recently used) the second loop will start with ‘hit’
  for (size_t i = 0; i < N; ++i)
  sum += a[i];
  double average = sum / N; for (size_t i = 0; i < N; ++i)
  a[i] -= average;

## Slide 17: Write Handling
Memory writes (store instructions) also need to update a cache
  If update only memory, the old data can be read from the cache later
There two main approached of write handling
  WriteThrough: always update both memory and cache
  WriteBack: update only cache, update memory at line eviction
Event | WriteThrough | WriteBack
Write hits cache | Update memory and cache | Update only cache (make line “dirty”)
Write misses cache | Option 1: Upload missing line into cache, update memory and cache Option 2: Update only memory | Upload missing line into cache, update only cache (make the line “dirty”)
A line is evicted | Do nothing | If the line is “dirty” write it back into memory

## Slide 18: Write Back example
to memory
from execution
cache set (16 ways)
data write
data read
fetched data
miss

## Slide 19: Small Summary
Where can a block placed?
  One place → direct mapped
  A few places → set associative
  Any place → full associative
What line is replaced on a miss?
  FIFO
  LRU
  Pseudo-LRU
How are writes handled?
  WriteThrough
  WriteBack
How is a block found?
  Indexing → direct mapped
  Limited search → set associative
  Full search → full associative

## Slide 20: The End