## Slide 1: Out-Of-Order Execution (part II)
Igor Smirnov 17 March 2018

## Slide 2: Refresher: OOO Exe
Superscalar – wide pipeline (4-5 in modern CPU)
Out-of-order – execute according real dependencies (“data flow”) rather than program order
Advantages:
  Exploit parallelism beyond adjacent instructions
  Hide long latencies (e.g., cache misses)
Compatibility: need to maintain visibility of in-order execution
  Precise exceptions, memory model, etc.

## Slide 3: Refresher: HW Instruction Window
Two states are supported: speculative and architectural
Instruction window (ROB) keeps all in-flight instructions and allows reconstruction of the original order at retirement
The large window the better performance
Limitations:
  False dependencies -> rename registers
  Branches -> accurate dynamic prediction
  Complex HW (so far we did not talk about that)

## Slide 4: RAT Restore
Each ROB entry saves previous register alias (history)
On flush, ROB is restores history
(1) r1  r4 / r7
(2) r8  r1 + r2
r1  r5 + 1
jump
(5) r6  r6 – r3
(6) r4  load [ r1 + r6 ]
(7) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
 |  | pr7 |  |  | pr21 |  | pr20 | pr3 | pr8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15
r1 was pr7
r8 was pr8
r1 was pr10
r6 was pr20
r4 was pr21
r7 was pr3
History

## Slide 5: Exception Handling

## Slide 6: Refresher: Exception Handling
In pipelined machine exceptions handling is complicated:
  Speculative code
  Simultaneous exceptions on different pipe stages
  Cancellation of consequent code
The solution was to postpone handling until writeback
  In OOO, we have retirement instead of writeback

## Slide 7: Exceptions
  At execution instruction that takes a fault/exception is marked
  Instructions older than the marked instruction are retired
  When the marked instruction retires – handle the fault
    Flush the ROB
    Initiate the handling code according to the type
    Re-fetch the faulting instruction and the subsequent instructions
Fetch
Retire
Instruction that caused exception
…
deleted

## Slide 8: Interrupts
If an interrupt occurs, let the oldest instruction retire, flush everything younger and proceed to handling:
F
D
A
E
F
D
A
F
D
A
E
F
D
A
E
R
F
D
A
E
R
F
D
A
F
D
A
F
D
A

## Slide 9: Scheduling

## Slide 10: Why Is ROB Complex?
The two complex searches though all ROB entries
  At allocation (once per each instruction): to identify producers of the instruction sources
  At scheduling (every cycle): to identify ready instructions and send them to execution
The larger ROB the longer search and large HW structures
  Prevents from doing ROB really large -> loose potential performance
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 11: Scheduler Queue
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 12: Scheduler Queue
Out-of-order execution
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
  All checks (allocation and scheduling) are performed on it
  Use ROB only for order reconstruction at retirement
PRF
EXE
Scheduler
Memory
ROB
SQ
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Write data
from decoder

## Slide 13: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
1
5
3
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At allocation of (3):
Search for Src1 producer
  Found in entry 1
    Mark dependency
Search for Src2 producer
  Found in entry 5
    Mark dependency
At least one is found -> not ready
false

## Slide 14: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At completion of (1,2):
Reset dependency to all consumers
For each entry check its readiness
false
true

## Slide 15: The End