## Slide 1: Memory Disambiguation
Igor Smirnov
24 March 2018

## Slide 2: Refresher: Write Handling
Memory writes (store instructions) also need to update a cache
  If update only memory, the old data can be read from the cache later
There two main approached of write handling
  WriteThrough: always update both memory and cache
  WriteBack: update only cache, update memory at line eviction
Event | WriteThrough | WriteBack
Write hits cache | Update memory and cache | Update only cache (make line “dirty”)
Write misses cache | Option 1: Upload missing line into cache, update memory and cache Option 2: Update only memory | Upload missing line into cache, update only cache (make the line “dirty”)
A line is evicted | Do nothing | If the line is “dirty” write it back into memory

## Slide 3: Store Execution
Stores are never performed speculatively
  There is no transparent way to undo them
Stores are also never re-ordered among themselves
  The store is dispatched only when
    The store has both its address and its data
    There are no older stores awaiting dispatch
Store commits its value to cache post retirement

## Slide 4: Load Execution
The target is to perform loads and their consumers speculatively
The only thing is check that load takes correct data
    (1) Mem[r1]  …
    …
    (6) …  Mem[r1]
Refresher: execution order is defined by data dependencies, which are detected at allocation
  If instruction(6) executes before (1), it will read a wrong value from memory

## Slide 5: Memory Dependencies
OOO engine can track dependency through registers, but not through memory
    (1) Mem[r1]  …
    …
    (6) …  Mem[r1]
Unlike register dependencies, memory dependency cannot be known at allocation
    (1) Mem[r2]  …
    …
    (6) …  Mem[r3]
Decision: load should wait until all the previous stores write into the memory (cache)
It works, but it is still too slow (stores write after retirement)
  If instruction(6) will executes before (1), it will read a wrong value from memory
  Registers r2 and r3 may have the same values

## Slide 6: Store Forwarding
Faster decision: load waits only if there is some older store with not calculated address
If addresses of all the previous stores are known and there is no intersection with them, then load can be executed
In case of intersection, the load is waiting until the data of the store is ready
Improvement: load can take data of the producing store bypassing cache, it is called Store Forwarding

## Slide 7: Intersection ≠ Forwarding
Forwarding condition is stronger than simple intersection
Example:
  sb $r1, 0x0($r3) // store byte
  sb $r2, 0x2($r3) // store byte
  lw $r4, 0x0($r3) // load FOUR bytes
Forwards (1)→(3) and (2)→(3) are not possible
However, (3) must wait for retirement of (2)
Can we forward from two stores? Theoretically, yes, but such programs are too rare to justify complexity

## Slide 8: Load and Store Buffer
Improvement: load does not wait if there is no intersection
  Need to wait until all previous stores calculate their address
  Then, check for intersection
  no intersection → load waits nothing
  forwardable intersection → load takes data from store
  intersection → load waits until the closest intersecting store writes data to cache/memory
Store can be at any ROB entry → any entry should be checkable
  Too large and slow HW
  On the other hand, not every instruction is load or store
  Like SQ, we can use smaller buffers for stores and loads only (store buffer or SB and load buffer or LB)
  All complex check of the address are done in LB and SB
  ROB just keeps the order of instructions

## Slide 9: SB and LB Operation
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
OK
yes
[0x35]
NO: (1)
0

## Slide 10: False Dependency from Store Data
If there is no overlapping load does not depend on store data
It depends only on store address
  To know that there is no overlapping load wait until all store addresses are calculated
Address is calculated when store is executed
But, store is sent to execution only all its sources (including data) are ready → there is a false dependency from data
(1) r1  …
(2) r2  …
(3) Mem[r1]  r2
…
(N) …  Mem[r3]
1
2
3
N
r1
r2
address
Example:
Data Flow Graph
  r3 != r1 → (3) and (N) are not overlapped
  False dependency:
  in fact, (N) does not need to wait (2)

## Slide 11: STA and STD
To remove false dependency in case of absence of overlapping store instruction is executed in two steps:
  Store address calculation (STA)
  Store data calculation (STD)
Load is waiting for STD only if it overlapped with STA
(1) r1  …
(2) r2  …
(3) addr  [r1]
(3’) Mem[addr]  r2
…
(N) …  Mem[r3]
1
3
N
r1
addr
Example:
Data Flow Graph
  Exist only if overlapping is detected
STA →
STD →
2
r2
3’
data

## Slide 12: SB and LB Operation: STA and STD
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
yes
[0x35]
0
Data
data: 0x100
0x100
(1)
yes
hit

## Slide 13: MD speculation
Load waits if there is some older STA with not calculated address
Can we make it faster? Yes, if load was dispatched speculatively
When STA is ready, perform check of all ‘skipped’ loads

## Slide 14: SB and LB Operation: speculation
(5) r6  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready? | OK?
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
… |  |  |  |  | 
M |  |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x01]
[0x25]
[0x35]
[0x25]
yes
[0x35]
Data
yes
(6) r7  r6 + r8
yes
hit

## Slide 15: MD speculation prediction
MD speculation requires decision making
The idea is to track history similar to branch prediction
Approach 1:
  assume “unknown” loads as speculative
  if the assumption is wrong, add PC of load to “blacklist”
  big overhead on rollbacks
Approach 2:
  assume “unknown” loads as non-speculative
  if there were no STAs to wait, add PC of load to “whitelist”
  moderate overhead as loads wait STAs in the beginning

## Slide 16: Summary
Stores write data in-order after retirement
Loads read data
  from cache, if they do not depend on non-retired stores
  from SB, if store forwarding is possible
  speculatively from cache/SB with mandatory checks
LB and SB track dependencies between loads and stores
LB and SB are responsible for performing 3 actions:
  Blocking loads dependent on stores
  Forwarding data from stores to loads
  Checking correction of load speculation

## Slide 17: The End