## Slide 1: Virtual Memory
Igor Smirnov
31 March 2018

## Slide 2: Acknowledgments
These slides contain material developed and copyright by:
Lihu Rappoport (MAMAS/Intel), 234267, L6-7

## Slide 3: Layers of Abstraction in Computer Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture

## Slide 4: Memory managing
address N
address 0
Initially, resources was managed manually by SW developer
  One program (= process) occupied the whole machine recourses
  There was no “external” programs with unknown code/requirements
Modern requirements
  Multi-tasking → not effective to give all resources to one process
  Many SW → cannot plan their co-existents anymore
How multiple process share the memory?
  What happens if a process tries to access memory of another process?
  What happens if processes need more memory and there is no free one?
  What happens if a new process is spawned?
Process A
Process B
Process C

## Slide 5: Virtual Memory (primary)
Virtual Memory (VM) is an approach that enables flexible, secure memory management
Provides isolation between processes
  Processes can concurrently run on a single machine
  VM prevents them from illegal accessing the memory of one another
  Allows convenient sharing of memory for communication when required
Provides illusion of large memory for each process
  VM size can be bigger than physical memory size
  VM decouples program from real size (can differ across machines)
Provides illusion of contiguous memory
  Programmers need not worry about where data is placed exactly

## Slide 6: Virtual Memory (secondary)
Allows for memory dynamic growth
  Can add memory to processes at runtime as needed
Allows for memory overcommitment
  Sum of VM spaces (across all processes) can be >> physical space
  Memory often one of the most costly parts in the system

## Slide 7: Virtual and Physical Address Space
Virtual address space
  Space used by the programmer (part of program visible state)
  Perfect abstraction = contiguous and completely belongs to the process
  Physical address space
  The real physical memory (e.g., DRAM) available in the computer
  Not known by the programmer (completely hidden by OS/HW)
  How to map virtual space to physical one?

## Slide 8: Basic Idea of VM
  Split both virtual and physical spaces into fixed size blocks called pages (commonly 4KB)
  Not need to place the whole virtual space into the computer → only pages used by the process
  Pages can be in physical memory or disk
  Memory acts as a cache for the secondary storage (disk)
  Process can use more pages that can be stored by physical memory
  Each process can access only their pages
Virtual Space
Physical Space
#page
#page
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
19 | 
40 | 
41 | 
Disk
#page
60 | 
122 | 

## Slide 9: Page Table
  To perform translation of virtual address into physical one, the special structure called Page Table (PT) is used
  It contains the flowing information for each page:
  Whether the page is in memory or on the disc
  Physical address of the page (if it is in memory)
  Was its data modified? → need for evictions
  Access rights (readonly, read-write, etc.) → security
  Each process has its own PT
  HW can use PT to translate addresses (= hit the table)
  But, all complex tasks (initialization, misses, evictions, etc.) are performed by OS

## Slide 10: Translation
 | Disc or memory? | Modified? | Access Rights? | Physical page number
0 |  |  |  | 
1 |  |  |  | 
… |  |  |  | 
… |  |  |  | 
 | Disc or memory? | Modified? | Access Rights? | Physical page number
0 |  |  |  | 
1 |  |  |  | 
… |  |  |  | 
… |  |  |  | 
Page Table
63 | 11 | 0
Virtual Page Number | Page Offset | 
Virtual Address
31 | 11 | 0
Physical Page Number | Page Offset | 
Physical Address

## Slide 11: TLB (translation lookaside buffer)
  The PT is too huge to be in HW → it is stored in memory
  There are multiple methods to compact it
  Each translation requires several memory access
  Needed for every load or store → too many!
Yes
No
TLB Hit ?
Access
Page Table
Virtual Address
Physical
Addresses
TLB Access
  TLB caches recently used PT entries
  speed up translation
  typically 64 to 256 entries
  usually 2 to 8 way associative
  TLB access time is faster than L1 cache access time

## Slide 12: PT, TLB and Cache
Yes
No
Access
TLB
Access
Page Table
In Memory
Virtual Address
Physical
Addresses
TLB
Hit ?
L2 Cache
Hit ?
No
L1 Cache
Hit ?
Yes
No
Data
No
Access
Memory
L2 Cache
Hit ?
Access
Cache

## Slide 13: Overlapped TLB & Cache Access
#Set is contained within the Page Offset
  The #Set is known immediately
  Cache can be accessed in parallel with address translation
  Once translation is done, match upper bits with tags
Limitation: Cache ≤ (page size × associativity)
Virtual Memory view of a Physical Address
Cache view of a Physical Address
0
Page offset
11
Physical Page Number
12
38
0
38
5
disp
tag
set
6
11
12

## Slide 14: Virtually-Addressed Cache
Cache uses virtual addresses (tags are virtual)
Address translation only done on a cache miss
    TLB is not in the path to cache hit
Two virtual pages mapped to the same physical page
    Must not reside in the cache together
    On a cache miss, use a reverse TLB to verify that no other cache line already in the cache mapped to the missed physical address
Flush cache on context switch
    Alternatively: add process ID as part of the tag
Cache
TLB
Main
Memory
VA
PA
CPU
data
data

## Slide 15: The End