## Slide 1: Multiprocessor Systems
Igor Smirnov
07 April 2018

## Slide 2: Refresher: Intel CPUs timeline
Chart: nm/MHz
| 1978 | 1982 | 1985 | 1989 | 1993 | 1995 | 1997 | 1999 | 2000 | 2002 | 2004 | 2006 | 2008 | 2011 | 2013
Freq | 0 | 8 | 16 | 25 | 60 | 150 | 233 | 450 | 1400 | 2000 | 3400 | 3000 | 3000 | 3000 | 3000
Process | 3000 | 1500 | 1000 | 1000 | 800 | 600 | 350 | 250 | 180 | 130 | 90 | 65 | 45 | 22 | 22
Pipeline Depth | 2 | 3 | 3 | 5 | 5 | 12 | 12 | 12 | 20 | 20 | 31 | 12 | 20 | 14 | 14
8086
80286
80386
80486
Pentium
Pentium Pro
PII
PIII
P4
Prescott P4
Power wall

## Slide 3: Motivation
Increasing performance becomes harder and less power efficient
Area budget can be divided in several ways:
  Single core — 6x area, 2.9 performance boost
  3 smaller cores — 2x area, 2.0 performance boost each — 6x area, 6.0 performance boost total!
Chart: Area
| 1 | 2 | 3 | 4 | 5 | 6 | 7
ST Perf | 1 | 2 | 2.5 | 2.75 | 2.875 | 2.9 | 2.9

## Slide 4: Thread-level parallelism
To achieve the best performance, workload should be parallelized to several threads
This is possible due to the thread-level parallelism (TLP)
    Unlike ILP, TLP is extracted manually by programmer
Threads can be extracted either from:
    The same application
    Different applications running simultaneously
    Operating system services
  Each thread is executed on single CPU

## Slide 5: Multiprocessor and Multicore
Originally, each CPU had its own chip
  Works well for independent workloads
  Otherwise for cooperative workloads (big latency for data exchange)
Later, multicore CPUs were introduced
  Caches and memory bus are shared between CPUs (cores)
  Thus, data exchange is made through the cache
CPU 1
CPU 2
Memory
CPU
Core 1
Core 2
Cache
Memory

## Slide 6: Memory Coherence in Multicore/multiprocessor System
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
Example:
Memory system must be coherent
  Cores should see memory identically
  Cores should see the latest state of memory
[X] ≡ 10
[X] ≡ 20
20
Memory: Mem[X] ≡ 10
Core 0: a = Mem[X] # a = 10
Core 1: Mem[X] = 20
Core 0: b = Mem[X] # b = 10
miss
miss
[X] ≡ 10
hit
Error: read the old value from the local cache
Problem: one core modifies data that another core has in its local cache
[X] ≡ 10
20

## Slide 7: Coherence protocol: MESI
 | Is the line valid? | Do we own this line? (others do not contain it) | Has it been modified?
Invalid | NO | NA | NA
Shared | YES | NO | NO
Exclusive | YES | YES | NO
Modified | YES | YES | YES
Coherency protocols describe how to handle writes and reads in a multi-core system in order to maintain memory coherence
The most famous one is MESI
  Define the four possible state of a cache line
  Describe transactions from one state to another (next foils)
There is no state when a line is modified and contained by other cores
To write a line, ownership should be obtained first

## Slide 8: MESI Operating Example
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
[X] ≡ 25
[X] ≡ 35
[X] ≡ 25
[X] ≡ 25
Memory: Mem[X] ≡ 25
Core 0: a = Mem[X] # a = 25
Core 0: Mem[X] ≡ 35
Core 1: b = Mem[X] # b = 35
  Snoop [X]
    Core 0 writeback [X]
Core 1: Mem[X] ≡ 45
  Request ownership for [X]
    Core 0 invalidate [X]
35
[X] ≡ 25
(1, 0)
E
M
35
35
[X]
(1, 1)
S
S
[X]
I
(0, 1)
[X]
M
45

## Slide 9: MESI State Diagram
R – read
W – write
Sh – line shared
!Sh – line not shared
SN – snoop
RO – request ownership
I
E
M
S
R or SN
R or W
R
SN or RO
W
SN
RO
R and !Sh
RO
R and Sh
SN
RO
W
W

## Slide 10: HPC Alternative Topologies
SMP — Symmetric Multi Processing
  Identical processing units
  Single shared memory, single bus, mesh interconnections
  Low scalability (systems with > 8 units will have performance problems)
NUMA — Non Uniform Memory Access. A CPU can access its own local memory faster than non-local memory.
  Highly scalable
  Requires special coherency protocols and OS support

## Slide 11: The End